SNDAN: SIGNAL ANALYSIS, GRAPHICS, PROCESSING, 
			AND SYNTHESIS ROUTINES FOR UNIX

Several programs are available for spectrum analysis, modification, and
resynthesis. One group of programs converts signal files into "analysis
files", which contain data for partial amplitudes, frequencies, and phases.
Another group is used to view data, either in signal or analysis form. A
third group includes programs to modify the analysis data. The fourth type
is used to synthesize signal files from analysis files.

Signal files can be of four types, headerless float, headerless short int,
NeXT with short ints or floats, and WAVE with short ints. These have
extensions .fp, .sh, .snd, and .wav, respectively. An *.fp file consists of
a sequence of 32-bit floating point numbers (IEEE standard). A *.sh file
consists of a sequence of 16-bit binary integer numbers. A *.snd file
consists of a NeXT standard header followed by a series of 16-bit integers
or 32-bit floats. A *.wav file consists of a WAVE header followed by a
series of 16-bit integers. .fp, .sh, and .snd files are assumed to be in
big-endian byte order, whereas .wav files are in little-endian order. Any
of the files can have 1 or 2 channels (samples alternate between channels 1
and 2), although currently most programs can only handle monaural sound
files. Stereo files can be converted to monaural using programs 'fixsnd' or
'fixwav' (left channel of 44100 stereo file to 22050 monaural file) or
'fixsndR' or 'fixwavR' (right channel of stereo file to monauarl file).

Signal files can be graphed using the program sp. It allows control of both
the time and amplitude scales of the graph. Graphs can be directly printed
or saved as .esp files and pasted into documents.

The program sextract can be used to extract individual sounds from a sound
file containing a sequence of these sounds and put them in separate sound
files.

Spectral analysis can be performed by either pvan (phase vocoder analysis)
or mqan (spectral tracking analysis). Two types of analysis files are
currently used. One (with extension .an) is restricted to harmonic
partials. All frequencies are assumed to be approximately harmonically
related to a fundamental, which is also the frequency of analysis. The
other (with extension .mq) can have frequencies of any relationship.
Another difference is that *.an files have a fixed number of partials
(harmonics), whereas with *.mq files, the number of partials varies with
time throughout the sound's duration. In both cases, each component has an
amplitude and frequency for each analysis frame; the .mq representation
includes a phase value for each frame. *.an representations are most
appropriate for sounds with fixed definite pitch. *.mq is better for sounds
with indefinite pitch, inharmonic partials, and/or variable pitch.

The program pvan directly produces an .an file from a signal file. It is
based on the well-known phase vocoder algorithm, except our version is
pitch-synchronous. That is to say, pvan aligns its window with the
specified fundamental frequency of the sound to be analyzed. gopvan is a
script which allows the user to enter information for pvan interactively
and then runs the pvan job in the background. In a similar fashion, mqan
(gomqan) directly produces a .mq file. It is based on the spectral tracking
algorithm of McAulay and Quatieri. Moreover, the tracks in .mq files can be
reduced to harmonics for .an files by a two-step procedure. The first step
is to process the .mq file using the program fcheck to determine its
fundamental frequency contour. The second step is to to process the
frequency contour and .mq data with the program harmformat to produce a
final .an file. The steps, mqan, fcheck, and harmformat are combined within
the script gomqhfan. The two methods of producing an .an file give similar
results, but there are advantages to each. pvan is more robust, but only
works well for sounds with a nearly constant pitch (i.e., less than +-2%
frequency variation). mqan -> fcheck -> harmformat is less robust, but it
is capable of handling wide pitch variations. Several script files are
available for the user to interactively give analysis parameters and to
automate the analysis processes. Examples are gomqan and gomqhfan.

Several graphics programs are available for viewing signals and spectral
data. On the NeXT and other computers, the data is shown using a Postscript
viewer (e.g., Preview on the NeXT or ghostview under X Windows). Whereas sp
is a program for viewing the waveform of a signal, monan is a program which
views spectral data of .an files, and mqdispp and mqdistr are programs for
viewing spectral data of .mq files. In any case, the graphs are based on
.eps files which are generated and these can be directly printed or pasted
into documents.

Modification of .an file data can be accomplished using monan. Synthesis of
.an files (using additive synthesis) can be done with addsyn, addsyn1,
addsyn2, adsyn3, monan, or by using the as.t instrument of Music 4C (a
separate package). Synthesis of .mq files (using additive synthesis) can be
done using the program mqsyn2.

Note that monan combines the activities of parameter viewing, modification,
and additive synthesis. AnView, a NeXT GUI application, combines these same
activities plus the activities of pvan and mqan.

For more details on how monan, pvan, mqan, sp and other programs work, see
the individual documentations for these programs.
___________________________________________________________________________
James Beauchamp 05/09/98